## Slide 1
I. Study of conductors
I.1. Conductor in electrostatic equilibrium:
A conductor is a medium (materials or substances) in which there are free charges (positive or negative) that can be set in motion under the action of an electric field..
A conductor is said to be in electrostatic equilibrium if no electrical charge is moving inside of this conductor.
The electrons are not subjected to any macroscopic force
I.2. Properties:
The electric field is zero inside an equilibrium conductor
A conductor in equilibrium constitutes an equipotential volume
The total charge is zero in any internal region of an equilibrium conductor.
Chapter I: Part III
The injected charges are located on the external surface

## Slide 2
The same properties are valid for a hollow conductor.
Qi=0
The injected charges are located on the external surface.
The field on the surface is perpendicular to this surface (Just outside a conductor, the electric field lines are perpendicular to its surface).
When we connect a charged conductor to another conductor, there will be an exchange of charges between the two in such a way that at the end of the transport, the two conductors constitutes the same equipotential volume.

## Slide 3
(S)
I.3. Electric field near the surface of a conductor (Just outside):
Coulomb's theorem.
At a point infinitely close to the surface, The field is normal to .
To find the field at this point, we apply Gauss's theorem:
Applying Gauss's theorem to this closed surface, we get:
The chosen Gaussian surface is a flattened cylinder, with one base located outside the surface and the other base at a depth such that the surface charge is completely inside the cylinder.

## Slide 4
Théorème: The electrostatic field just outside (near) a conductor carrying a charge with a surface charge density is:
At the crossing of the surface of a conductor, by continuity, the Field varies from 0 (inside) to (outside) through the value on the real surface of the conductor.
Remarks:
This last expression of the field will be used for the calculation of the electrostatic pressure.
I.4. Electrostatic pressure:
Let « » a surface element carrying a charge with
The field exerts, on the charge, a force:
Electrostatic pressure is given by:
Layer Superficial
Inside
Outside

## Slide 5
I.5. Power ot the pointed conductors:
Considering Two Conductive Spheres with radius and (< ), connected by a long conducting wire.
The two spheres are brought to the same potential:
The sphere with the smallest radius carries the greatest density of charges.
A tip (R very small) carries a large charge density.

## Slide 6
A very pointed conductor has a large charge concentration at the point. The electric field is very strong at the point and can exert a force large enough to transfer charge on or off the conductor.
Lightning rods are used to prevent the buildup of large excess charges on structures and, thus, are pointed.

## Slide 7
Consider an insulated conductor in electrostatic equilibrium carrying a charge Q distributed over its outer surface with Surface charge density such as:
I.6. Capacity of a conductor:
If the charge Q increases, the density σ increases proportionally:
The potential created by Q at a point M in space:
We deduce that the ratio between the charge and the potential to which the conductor is brought, given by depends only on the geometry of the conductor, it is called the conductor's own capacity.

## Slide 8
Example:
Find the own capacity of a sphere of radius R carrying a charge Q uniformly distributed over its surface.
At a point M on the surface of the sphere, the potential is given by:
I.7. Potential (Internal) energy of an isolated charged conductor:
To bring a charge Q to a conductor, initially neutral, it is necessary to provide a work "W"
The variation of potential energy undergone by an elementary charge dq , brought back from infinity (chosen as a reference of potential) to the conductor:
The potential energy of the conductor when it reaches its full charge q is:
With

## Slide 9
I.8. Phenomenon of influence between electrical conductors:
An electrical conductor is said to be neutral if
A neutral conductor placed in an electric field polarizes.
Partial influence:
Let be a neutral conductor placed in a field
Negative charges move in the opposite direction of the field.
On either side of the conductor appear positive and negative charges in equal quantities.
A new field , due to this distribution of charges, is created and comes to superimpose the field .
Inside the conductor, the charges do not stop moving until the field
The conductor is again in equilibrium in a polarized state
The charge is not varied, there has been a modification in the distribution of the charge.

## Slide 10
+
+
+
No Influence

## Slide 11
If the conductor is kept at a constant potential (e.g. zero):
+
The ground and conductor (A) form a single conductor.
(A)
V=0
The potential of the conductor (A) becomes zero.
The positive charges are pushed back into the ground and the negative charges remain trapped by the field created by the body (B).
There is no field line leaving the conductor (A).

## Slide 12
Influence in return (Feedback):
The influencing charge is distributed on the conductor (B).
There is a feedback influence of (A) on (B)
We say that there is mutual influence

## Slide 13
Total Influence:
We speak of total influence when all field lines starting from (B) end up at (A).
Let (B) a conductor carries a charge and (A) A hollow conductor in equilibrum
Let's choose the surface passing inside (A) and we apply Gauss's theorem:
After the influence, a charge negative appears on the internal surface of (A) and a positive charge on the external surface
If (A) and isolated and neutral initially, there will be:
If (A) and isolated and initially carries a charge , There will be:

## Slide 14
Let a conductor (A) be held at zero potential (V=0)
I.8. Capacitors:
Let a conductor (B) be held at a potential carries a charge :
The influence of (B) leads to the appearance of negative charges on (A).
These negative charges of (A) in turn influence (B) on which new charges appear from the generator in order to keep constant.
There is condensation of charges on (B) and its capacity is given by:
Conductors (A) and (B) form a capacitor represented by:
We call : Capacitor charge
depends only on the shape of the conductor and the nature of the air between them
If the two conductors are brought closer together, the capacity becomes greater.

## Slide 15
Method of calculating the capacitance of a capacitor:
1- Calculate the electric field at any point inside the capacitor.
2- Deduct the potential difference between the two conductors.
3- effect the report :
Examples:
1- Plane capacitor:
Formed by two infinite parallel conductive planes, separated by a distance "e".
Field created by (A) :
Field created by (B) :
Field created between (A) and (B):

## Slide 16
2- Cylindrical capacitor:
The field created between the two cylinders:
Gauss's theorem:
The difference in potential between the two cylinders:
Capacitance:

## Slide 17
3- Spherical capacitor:
The field created between the two spheres:
Using Gauss's theorem, we find:
The potential between the two spheres:
We find:
Capacitance:

## Slide 18
Potential energy of a capacitor (stored in a capacitor):
+
Let be a capacitor with a capacitance "C" formed by two armatures A and B
Knowing that:
In general, for a set of capacitors carrying charges under different potentials :

## Slide 19
Capacitor Association
1- Parallel association:
All capacitors are subject to the same difference in potential

## Slide 20
1- Series Association :
All capacitors carry the same charge Q: